## Slide 1
Neighborhood Traffic Management Program (NTMP)
City of Raleigh
Department of Transportation
Traffic Calming 101

## Slide 2: Agenda
Neighborhood Traffic Management Program (NTMP)
  Traffic Calming Overview
  Traffic Calming Process & Project Eligibility
  Traffic Calming Treatments
  Project Areas
  Questions & Contact Information

## Slide 3: Traffic Calming Overview
What is traffic calming?
  Combination of measures that reduce the negative effects of motor vehicle use, alter driver behavior, and improve conditions for non-motorized street users (USDOT)
What is Raleigh’s response to address the traffic calming need?
  The City of Raleigh adopted the Neighborhood Traffic Management Program (NTMP) and gave it three tools
    Multiway Stop Conversions – specifically used for intersection safety
    Speed Limit Reductions – to better set more appropriate speed limits in residential settings
    Traffic Calming Projects – to encourage speed compliant behavior when signage is not enough
What is the vision of the NTMP?
  To improve safety, improve speed compliance, and enhance the quality of life along residential streets in Raleigh’s neighborhoods

## Slide 4: Traffic Calming Process

## Slide 5: Traffic Calming Project Process
Step 1
  Teach about Traffic Calming as a concept
  Present staff’s best practice layout/design
  Paint layout on street to help visualize project footprint
  Receive resident design feedback
  Answer resident Questions
Step 2
  Present updated layout/design based on feedback
  Receive resident design feedback
  Answer resident Questions
Step 3
  Ballot Neighborhood asking “Do you want this Project Constructed?”
    On-street: 70% approval rating
    Neighborhood: 60% approval rating

## Slide 6: Traffic Calming Treatment Selection
Why are certain treatments used on one street and not the other?
  Traffic calming projects work to stay 100% within the existing street footprint. For that reason, existing street widths are a major factor in device selection
    Streets that are < 31’ wide can only support vertical treatment options. The street is not wide enough to allow for effective horizontal measures
    Streets that are > 31’ wide can support both vertical and horizontal traffic calming treatments options and staff works to propose the best treatment for each unique situation
    Proximity to Fire Stations and designated emergency routes are subject to additional restrictions on treatment choice and potentially result in a street being not eligible for any traffic calming project
What is the design process?
  The design and treatment choice is heavily influenced by neighborhood feedback and suggestions. If a certain device is approvable from an engineering perspective and generally desired by the neighborhood, it is incorporated into the design

## Slide 7: Traffic Calming Treatments
Speed Humps
Speed Cushion
Speed Table
Vertical Treatment Types

## Slide 8: Traffic Calming Treatments
Horizontal Treatment Types
Neighborhood Traffic Circle
Curb Bump Out
Chicane

## Slide 9: Raleigh Traffic Calming Projects
Completed Projects - 68
  Average Speed Diff: -8.78 mph
    Average After 85th% Speed vs Speed Limit: +.21 mph
  Average Volume Diff: -576.57 vehicles per day
    Average Change in Vol: -24.56%
  Average Change in Crashes: -74.17%
Projects in Construction - 15
Approved for Construction - 17
  17 expected construction: 2025
Projects in Engagement/Design - 20
  Neighborhood Vote: Oct/Nov 2024
Eligible Future Projects - 118
  Goal of up to 20 project offerings each year

## Slide 10
Questions?
Contact Information:
NTMP@raleighnc.gov
919-996-4066