## Slide 1
TRANSPORTATION
Preliminary Traffic Calming Design & Public Comment

## Slide 2: How do we approach the traffic calming design?
Consistent treatment placement along entire street
  400’ – 700’ spacing of treatments
  Close spacing is used for streets with a higher speed compliance issue
  Target pedestrian heavy amenities to increase safety, such as access to the retail at the intersection of Harps Mill Rd with Litchford Rd
Targeted placement to fix a speed related crash issue
  If a pattern of speed related crashes is identified, targeted treatment placement can eliminate that crash pattern
  If no pattern is identified locationally, but multiple speed related crashes have occurred, consistent treatment spacing can help eliminate crashes along an entire street

## Slide 3: Treatment Limitations
Your street’s width will determine what types of treatments can be placed
  Harps Mill Rd is approximately 41’ wide
  Based on this street width and roadway design, vertical and horizontal traffic calming elements eligible. Based on the street context, vertical treatments are being proposed as part of this project

## Slide 4: Speed Humps (vertical)

## Slide 5: Speed Humps (vertical)
Can be the most effective
Fast installation time/Less impact during construction
Versatile placement options based on compact footprint
Pros
Cons
Does not contrast as much with existing roadway
Impact to driving comfort
Creates slight delay in emergency service’s response times

## Slide 6: Speed Cushions (vertical)
*Speed Cushion dimensions vary based on roadway dimensions

## Slide 7: Speed Cushions (vertical)
Can be as effective as speed humps
Relatively low impact installation timeline, but slightly slower than a standard hump as more labor is required
Versatile placement options based on compact footprint
Slightly faster emergency service’s response times due to tire slits for larger vehicles
Pros
Cons
Does not contrast as much with existing roadway
Reduced driving comfort
There is still some level of delay to emergency service’s response times when compared with no treatment

## Slide 8: Evaluation Data

## Slide 9: Design Process
Based on the speed progression and crash issue identified along Harps Mill Rd, we are proposing treatment spacing of approximately 400’ – 500’ intervals
No reoccurring speed related crash issues were identified. Speed reduction will be the focus of this effort

## Slide 10: Project Goal
The project will be deemed effective if 85% of drivers are going at or below the 25 mph speed limit and top driver speed is capped at around 5-7 mph over the speed limit
  Based on your location, Johnsdale Rd and Whitehall Ave are the closest completed traffic calming project to you with this style of completed project. We encourage you to go drive these streets yourself to experience the final project.
Once the project has been completed for approximately 6 months, an after-study will be performed to measure project effectiveness

## Slide 11: Public Comment
What are your thoughts on the proposed design?
  Should we place more or less treatments along the street?
Have we adequately addressed problem areas you see?
  Should we place another traffic calming treatment in a targeted location?
What are your thoughts on the mix of treatments being proposed?
What other questions, comments, suggestions do you have?

## Slide 12
Please direct all comments and questions to staff using the PublicInput portal for Harps Mill Rd - E. Staff will respond and we can have a neighborhood wide conversation.