## Slide 1
TRANSPORTATION
Preliminary Traffic Calming Design & Public Comment

## Slide 2: How do we approach the traffic calming design?
Consistent treatment placement along entire street
  400’ – 700’ spacing of treatments
  Close spacing is used for streets with a higher speed compliance issue
  Target pedestrian heavy amenities to increase safety, such the Crabtree Creek greenway trail and existing bike lanes
Targeted placement to fix a speed related crash issue
  If a pattern of speed related crashes is identified, targeted treatment placement can eliminate that crash pattern
  If no pattern is identified locationally, but multiple speed related crashes have occurred, consistent treatment spacing can help eliminate crashes along an entire street

## Slide 3: Treatment Limitations
Your street’s width will determine what types of treatments can be placed
  Milburnie Rd is approximately 41’ wide
  Based on this street width, lack of intersections, and existing bike infrastructure, vertical traffic calming elements are appropriate and are being proposed as part of this project
  Due to the 30-mph speed limit and relatively high vehicular volumes, speed tables are the most appropriate vertical traffic calming device

## Slide 4: Speed Table (vertical)

## Slide 5: Speed Table (vertical)
Can be the most effective
Fast installation time/Less impact during construction
Versatile placement options based on compact footprint
Pros
Cons
Does not contrast as much with existing roadway
Impact to driving comfort
Creates slight delay in emergency service’s response times

## Slide 6: Evaluation Data

## Slide 7: Design Process
Based on the speed progression and high vehicular volumes along Milburnie Rd, we are proposing treatment spacing of approximately 500’ – 600’ intervals
A speed related crash issue was not identified through our evaluation. The focus of this project is speed reduction

## Slide 8: Project Goal
The project will be deemed effective if 85% of drivers are going at or below the 30 mph speed limit and top driver speed is capped at around 5-7 mph over the speed limit
  Based on your location, King Charles Rd, Milburnie Rd – W, and Glascock St are the closest completed traffic calming project to you with this style of completed project. We encourage you to go drive these streets yourself to experience the final project.
Once the project has been completed for approximately 6 months, an after-study will be performed to measure project effectiveness

## Slide 9: Public Comment
What are your thoughts on the proposed design?
  Should we place more or less treatments along the street?
Have we adequately addressed problem areas you see?
  Should we place another traffic calming treatment in a targeted location?
What other questions, comments, suggestions do you have?

## Slide 10
Please direct all comments and questions to staff using the PublicInput portal for Milburnie Rd - E. Staff will respond and we can have a neighborhood wide conversation.